## Slide 1
SPEC2PRIMITIVES / PHASE 4 / PURPOSE
Phase 4: ground the product,
then assign an arm
Current code + saved trace • 09 Sep 2026 • Sources in speaker notes
01 / 09
Connect an assembly requirement to observed facts and a supported assignment.
INPUT
“assemble medium gear.”
Requirement + approved evidence
PA INVESTIGATION
What is here?
What should be
assembled?
Current state + desired relationship
OUTPUT
Grounded product
context + selected arm
Evidence, ontology and position checks
10-minute technical walkthrough • PA = ProductAgent • RA = RobotAgent
Notes: Target duration: 45 seconds.
Phase 4 turns an assembly requirement into a grounded product goal and an arm assignment. PA means ProductAgent. It investigates what the user wants, which observed objects are relevant, how the product is currently configured, and what relationship should hold after assembly. The output links those claims to their evidence and records which arm passed the required position checks. I will explain the implemented flow using the saved requirement, “assemble medium gear.” In that run, PA selected xarm6. That selection is backed by modeled position planning. Primitive order, robot targets and later execution belong to subsequent stages. The central question for these ten minutes is how the system connects a short requirement to evidence that a downstream RobotAgent can use.
Sources relative to cais_spade_llm/spec2primitives/:
- Implemented phase boundaries: IMPLEMENTATION_PLAN.md:5
- PA orchestration: agents/pa/production_grounding.py:1481
- Saved completion: contexts/interaction_116f33c8cce64d33b0066891bf228572/interaction_record/context_completion_0001.json
This is a presentation of inspected code and a saved trace. No new runtime experiment was run.

## Slide 2
SPEC2PRIMITIVES / PHASE 4 / IMPLEMENTATION MAP
Phase 4 builds a grounded product context
Current code + saved trace • 09 Sep 2026 • Sources in speaker notes
02 / 09
4.0
Ontology
foundation
Supplied PPR TBox
Interaction ABox
Workcell authorities
4.1
Document
evidence
Approved page index
PA-authored queries
Cited interpretations
4.2
CAD + RGB-D
Observed candidates
Morphology + size
Calibrated locations
4.3
Evidence
contracts
Typed records
Exact references
Hashes + uncertainty
4.4
Goal +
assignment
target_feature
Pairwise relationships
MoveIt arm checks
PA chooses the evidence order. Phase 4.3 contracts apply throughout.
HANDOFF TO PHASE 5 Selected RA context → primitive_steps → bounded validation
Notes: Target duration: 60 seconds.
The implementation divides Phase 4 into five boundaries. Phase 4.0 supplies the PPR TBox and initializes an interaction ABox. The TBox is the supplied vocabulary and its constraints; the ABox contains facts for this interaction. PA creates instances under that vocabulary rather than discovering a new schema. Phase 4.1 makes approved document pages available and supports questions authored by PA. Phase 4.2 provides CAD and RGB-D evidence: segmentation, morphology, measurements, layout and calibrated locations. Phase 4.3 defines typed evidence, provenance and validation contracts across the investigation. Phase 4.4 combines a complete target_feature proposal, deterministic checks, pairwise assembly relationships and required arm assignment. These labels describe implementation boundaries, rather than a fixed sequence of model tool calls. Phase 5 begins from the completed grounding and captures context from the exact selected RA before composing primitive_steps.
Sources relative to cais_spade_llm/spec2primitives/:
- Implemented phase table: IMPLEMENTATION_PLAN.md:5
- Interaction entry point: agents/pa/context_interaction.py:64
- Selected-RA handoff: agents/ra/context_handoff.py:304
This is a presentation of inspected code and a saved trace. No new runtime experiment was run.

## Slide 3
SPEC2PRIMITIVES / PHASE 4 / CONTROL FLOW
PA decides what evidence to request next
Current code + saved trace • 09 Sep 2026 • Sources in speaker notes
03 / 09
PA
Choose the next question
and evidence source
Evidence tools
retrieve • query_document
compare_cad_size
analyze_candidate_layout
PA proposal
target_feature
Current + desired states
Assembly relationships
Host validation
Correctable reference / missing-location feedback
CONFIGURED LIMITS 24 evidence operations / 6 proposals
Accepted → ontology commit
Notes: Target duration: 75 seconds.
The production entry point creates an evidence investigation and presents approved source handles to PA. PA chooses among four tools. retrieve obtains a document index, CAD measurements or an observation bundle. query_document asks a task-specific question about approved document pages. compare_cad_size reports candidate measurements against a selected CAD file. analyze_candidate_layout measures relationships among selected candidates in the same view. PA can use several operations before submitting one complete target_feature. The configured investigation limits are twenty-four evidence operations and six proposals. These are ceilings, not a required number of calls. Correctable unissued references or missing state locations can trigger feedback and another proposal while retaining the pinned observation. Some invalid outputs stop immediately; unchanged failures stop as no progress. Genuine requirement ambiguity can request user clarification. In the saved example PA used nine evidence operations and one proposal. The host does not prescribe that evidence order.
Sources relative to cais_spade_llm/spec2primitives/:
- Investigation and bounded correction: agents/pa/production_grounding.py:1481
- Configured budgets: config/model_runtime.json:2
- Saved tool usage: contexts/interaction_116f33c8cce64d33b0066891bf228572/interaction_record/turn_0001.json
This is a presentation of inspected code and a saved trace. No new runtime experiment was run.

## Slide 4
SPEC2PRIMITIVES / PHASE 4 / EVIDENCE
Documents, CAD and RGB-D contribute different facts
Current code + saved trace • 09 Sep 2026 • Sources in speaker notes
04 / 09
01
DOCUMENTS
Intended relationships
Approved pages + figures
PA-authored query
Citations + uncertainty
Supports what should be assembled.
02
CAD
Candidate geometry
Measured mesh dimensions
All-candidate size comparison
No tool-selected winner
Supports shape and size comparison.
03
RGB-D
Observed evidence
Neutral segments + morphology
Bounds, centroids and layout
Approved frame conversion
Supports where observed objects are.
PA connects part identity, task role and the desired assembly relationship.
Notes: Target duration: 75 seconds.
Each evidence stream supplies a different part of the grounding problem. Document retrieval creates a source index with page text, rendered images and provenance. A document VLM answers PA's question with citations and uncertainty. CAD preprocessing measures the approved mesh, with units converted for geometry calculations. The active size comparison returns measurements for every evaluated candidate; it does not select a winner. RGB-D preprocessing deprojects valid depth, and neutral segmentation yields candidate bounds and centroids. An observation VLM describes candidate morphology and uncertainty without assigning task roles. The layout tool reports same-view positions, displacements, distances and collinearity. Approved calibration later maps selected observations into the frame used for arm checks. PA combines these facts to interpret identity and task role. Document relationships alone do not establish current installation. Source and candidate presentation handles are randomized and retained for audit; simulator object identities and evaluator answers are excluded from recognition.
Sources relative to cais_spade_llm/spec2primitives/:
- Active evidence production: agents/pa/production_grounding.py:1709
- Document tools: tools/document_evidence/README.md:3
- Perception tools: tools/rgb_d_cad_grounding/README.md:3
- Recognition evidence boundary: AGENTS.md:156
This is a presentation of inspected code and a saved trace. No new runtime experiment was run.

## Slide 5
SPEC2PRIMITIVES / PHASE 4 / VALIDATION
The host checks contracts; PA owns meaning
Current code + saved trace • 09 Sep 2026 • Sources in speaker notes
05 / 09
PA authors
Part identities and task roles
Current and desired state meaning
Pairwise assembly relationships
Coverage of the user requirement
Host validates
Schema + supplied PPR constraints
Exact citations and typed bindings
Hashes and source provenance
Required current / desired locations
Semantic correctness needs separate evaluation. Source uncertainty stays visible.
Notes: Target duration: 60 seconds.
There are two responsibilities here. PA interprets the evidence: which candidate is the required part, which observed reference has the destination role, what the current and desired states mean, and whether the requirement is covered. The host validates the proposal's structure, allowed ontology terms, exact references, typed values and evidence hashes. It also requires coordinate-bearing state values in both states for the planning consumer. A rejected target proposal never contributes its proposed assertions. Supported correction preserves the observation and returns generic feedback, without giving PA the task answer. Source uncertainty is derived from typed evidence and retained with accepted claims. The current production path has no second independent semantic reviewer. Consequently, a deterministic pass establishes the checked contracts and evidence lineage. Semantic correctness and model performance still require separate evaluation. A later arm-assignment failure can leave the grounded product visible while preventing completion.
Sources relative to cais_spade_llm/spec2primitives/:
- Proposal validation: agents/pa/ontology_grounding.py:305
- Evidence-preserving commit: agents/pa/ontology_grounding.py:433
- Correction and incomplete outcomes: agents/pa/production_grounding.py:1570
- Current reviewer boundary: IMPLEMENTATION_PLAN.md:43
This is a presentation of inspected code and a saved trace. No new runtime experiment was run.

## Slide 6
SPEC2PRIMITIVES / PHASE 4 / RECORDED WALKTHROUGH
Saved example: “assemble medium gear.”
Current code + saved trace • 09 Sep 2026 • Sources in speaker notes
06 / 09
Observed candidate crop
Observed assembly workspace
PA binding: medium gear
PA’S SAVED INTERPRETATION
current_state
medium gear separate from
its intended middle gear shaft
desired_state
medium gear mounted on the
middle gear shaft of the gear plate
The shaft provides an observed reference; a final gear pose is still unspecified.
Saved trace: 9 evidence operations • 1 proposal • Images are observed references; task correctness was not independently scored here.
Notes: Target duration: 75 seconds.
This example comes from a saved interaction, rather than a new experiment conducted for this presentation. On the left is the saved candidate crop that PA bound as the medium gear. The center image is the observed assembly workspace. PA's saved current-state statement says the medium gear is separate from its intended middle gear shaft on the gear plate. The desired state describes the required mounted relationship. Its coordinate-bearing value is named “observed middle gear shaft destination reference.” The saved statement explicitly distinguishes that observed shaft reference from a measured final gear pose. PA retrieved document, observation and CAD evidence; compared candidate sizes; asked which shaft should receive the medium gear; and requested same-view layout evidence. That trace contains nine evidence operations and one target proposal. These images show the observations associated with the saved interpretation. They do not show a completed assembly. The trace is useful for explaining behavior, while an independent evaluator would still need to assess whether the interpretation is correct.
Sources relative to cais_spade_llm/spec2primitives/:
- Saved target_feature: contexts/interaction_116f33c8cce64d33b0066891bf228572/products/grounding/ontology_grounding/proposal_0001.json
- Saved investigation counts: contexts/interaction_116f33c8cce64d33b0066891bf228572/interaction_record/turn_0001.json
- PA document question: contexts/interaction_116f33c8cce64d33b0066891bf228572/interaction_record/tool_call_0008.json
- PA layout request: contexts/interaction_116f33c8cce64d33b0066891bf228572/interaction_record/tool_call_0009.json
- Saved gear crop: contexts/interaction_116f33c8cce64d33b0066891bf228572/products/grounding/rgb_d_cad_grounding/observation_review_0001/view_0003_candidate_0003_0002.png
- Saved workspace RGB: contexts/interaction_116f33c8cce64d33b0066891bf228572/products/observations/observation_0002/cam_assembly_rgb.png
This is a presentation of inspected code and a saved trace. No new runtime experiment was run.

## Slide 7
SPEC2PRIMITIVES / PHASE 4 / ONTOLOGY
One desired relationship links two grounded features
Current code + saved trace • 09 Sep 2026 • Sources in speaker notes
07 / 09
Assembly: gear plate assembly
hasAssemblyFeatureAssociation
AssemblyFeatureAssociation
state_names: ["desired_state"]
relatesAssemblyFeature
relatesAssemblyFeature
medium gear central bore
Binding: current_state → medium gear current location
middle gear shaft mounting surface
Binding: desired_state →
observed middle gear shaft destination reference
Association membership and endpoint observation bindings are independent.
Notes: Target duration: 60 seconds.
The ontology preserves a pairwise representation. In this saved proposal, the owning Assembly is named “gear plate assembly.” It has an AssemblyFeatureAssociation relating exactly two AssemblyFeature endpoints: “medium gear central bore” and “middle gear shaft mounting surface.” The association's state_names contains desired_state, which says this is the intended relationship. Each endpoint has its own observation binding. In this saved run the gear endpoint binds to a current_state value, and the shaft endpoint binds to the desired_state destination reference. Relationship membership and endpoint bindings are separate concepts; the general contract also permits both endpoint observations to come from current_state. Multiple relationships create separate pairwise association individuals. The host preserves exact names and reuses owners only by exact identity. These assertions describe the product and the required relationship. They do not prescribe approach, grasp, lift or insertion order; RA determines primitive order later.
Sources relative to cais_spade_llm/spec2primitives/:
- Fixed terms and state membership: ASSEMBLY_ONTOLOGY.md:5
- Saved pairwise association: contexts/interaction_116f33c8cce64d33b0066891bf228572/products/grounding/ontology_grounding/proposal_0001.json
- Pairwise contract regression: tests/test_pa_completion.py:1179
This is a presentation of inspected code and a saved trace. No new runtime experiment was run.

## Slide 8
SPEC2PRIMITIVES / PHASE 4 / RESOURCE ASSIGNMENT
PA checks every capable arm before selecting
Current code + saved trace • 09 Sep 2026 • Sources in speaker notes
08 / 09
Same evidence for both arms: 2 current references + 1 desired reference
Arm
All bound positions
Mean distance*
xarm6
accepted
0.549 m
ur5e
accepted
0.627 m
*Mean straight-line distance from the live TF base
to the grounded current_state locations.
MoveIt GetMotionPlan
Live robot state + scene
Configured group / TCP
5 mm position tolerance
Unconstrained tool orientation
PA selected xarm6 • Accepted position plans are required; distance provides an advisory preference.
Notes: Target duration: 90 seconds.
Once the target is committed, allocation gathers every grounded coordinate-bearing value in current_state and desired_state. PA must check every configured capable arm against those same locations. This saved example has two current references and one desired reference; the desired shaft is also a current reference, so the sets contain a repeated physical location. The owned MoveIt adapter calls GetMotionPlan using the configured planning group and end-effector link, live robot state and the available collision scene. The position tolerance is five millimeters and tool orientation is unconstrained. No RobotAgent is activated and no motion is executed during these checks. Both xarm6 and ur5e returned accepted checks. Their recorded mean base-to-current-location distances were 0.549 and 0.627 meters, respectively. PA selected xarm6. Distance is advisory straight-line evidence, not path length or execution time. A farther accepted arm needs supporting task evidence; equal or unavailable distances supply no preference. Rejected or unavailable planning cannot be overridden by proximity. Omitted arm checks get one correction attempt. A planning failure means no plan was validated by that search, rather than a proof of mathematical unreachability.
Sources relative to cais_spade_llm/spec2primitives/:
- Allocation orchestration: agents/pa/production_grounding.py:1790
- PA selection policy: agents/pa/production_grounding.py:2394
- MoveIt request: adapters/moveit_plan_only.py:146
- Proximity calculation: agents/pa/resource_proximity.py:75
- xarm6 check and distance: contexts/interaction_116f33c8cce64d33b0066891bf228572/interaction_record/allocation_tool_call_0001.json
- ur5e check and distance: contexts/interaction_116f33c8cce64d33b0066891bf228572/interaction_record/allocation_tool_call_0002.json
- Saved arm selection: contexts/interaction_116f33c8cce64d33b0066891bf228572/products/grounding/resource_selection/selection_0001/resource_selection_record.json
This is a presentation of inspected code and a saved trace. No new runtime experiment was run.

## Slide 9
SPEC2PRIMITIVES / PHASE 4 / COMPLETION + CLAIMS
Completion hands grounded evidence to Phase 5
Current code + saved trace • 09 Sep 2026 • Sources in speaker notes
09 / 09
Grounded product
target_feature
Current + desired states
Pairwise relationships
Arm assignment
Selected resource
All-arm planning evidence
Assignment assertions
Traceable completion
Sources + typed records
Hashes + context snapshot
Persistent uncertainty
validation_scope:
moveit_state_location_reachability
motion_validation_performed: true
motion_executed: false
PHASE 5 CONTINUES WITH
Selected RA context → primitive_steps
Target calculations + modeled validation
Assembly success requires execution and independent outcome evidence.
Notes: Target duration: 60 seconds.
A successful Phase 4 result packages the accepted target proposal, source and typed evidence, selected arm, all-arm check lineage, assignment delta and final product context. The completion writer pins references and hashes so recovery can check that the evidence chain still matches. An incomplete assignment cannot authorize the next stage. In the saved completion, validation_scope is moveit_state_location_reachability, motion_validation_performed is true, and motion_executed is false. The next explicit boundary activates or reuses only the exact selected RA and captures its context. RA then authors primitive_steps and obtains the targets needed by those operations within Phase 5's bounded process. The defensible claim for Phase 4 is an evidence-linked product context with an arm assignment supported by modeled position planning. Grasping, attached-part motion, insertion, force and manufacturing tolerances are outside those position checks. Execution and independent outcome observation are needed before claiming assembly success.
Sources relative to cais_spade_llm/spec2primitives/:
- Completion writer: agents/pa/grounding_contracts.py:1705
- Completion recovery: agents/pa/grounding_contracts.py:2076
- Saved completion fields: contexts/interaction_116f33c8cce64d33b0066891bf228572/interaction_record/context_completion_0001.json
- Next boundary: selected RA: agents/ra/context_handoff.py:304
This is a presentation of inspected code and a saved trace. No new runtime experiment was run.